## Slide 1: P&S Modern SSDs FLIN: Enabling Fairness and Enhancing Performance in Modern NVMe Solid State Drives
Arash Tavakkol, Mohammad Sadrosadati, Saugata Ghose,
Jeremie S. Kim, Yixin Luo, Yaohua Wang, Nika Mansouri Ghiasi,
Lois Orosa, Juan Gómez-Luna, Onur Mutlu
ISCA 2018

## Slide 2: Executive Summary
Modern solid-state drives (SSDs) use new storage protocols (e.g., NVMe) that eliminate the OS software stack
  I/O requests are now scheduled inside the SSD
  Enables high throughput: millions of IOPS
OS software stack elimination removes existing fairness mechanisms
  We experimentally characterize fairness on four real state-of-the-art SSDs
  Highly unfair slowdowns: large difference across concurrently-running applications
We find and analyze four sources of inter-application interference that lead to slowdowns in state-of-the-art SSDs
FLIN: a new I/O request scheduler for modern SSDs designed to provide both fairness and high performance
  Mitigates all four sources of inter-application interference
  Implemented fully in the SSD controller firmware, uses < 0.06% of DRAM space
  FLIN improves fairness by 70% and performance by 47% compared to a state-of-the-art I/O scheduler

## Slide 3: Background: Modern SSD Design Unfairness Across Multiple Applications in Modern SSDs FLIN: Flash-Level INterference-aware SSD Scheduler Experimental Evaluation Conclusion
Outline

## Slide 4: Internal Components of a Modern SSD
Back End: data storage
  Memory chips (e.g., NAND flash memory, PCM, MRAM, 3D XPoint)

## Slide 5: Internal Components of a Modern SSD
Back End: data storage
  Memory chips (e.g., NAND flash memory, PCM, MRAM, 3D XPoint)
Front End: management and control units

## Slide 6: Internal Components of a Modern SSD
Back End: data storage
  Memory chips (e.g., NAND flash memory, PCM, MRAM, 3D XPoint)
Front End: management and control units
  Host–Interface Logic (HIL): protocol used to communicate with host

## Slide 7: Internal Components of a Modern SSD
Back End: data storage
  Memory chips (e.g., NAND flash memory, PCM, MRAM, 3D XPoint)
Front End: management and control units
  Host–Interface Logic (HIL): protocol used to communicate with host
  Flash Translation Layer (FTL): manages resources, processes I/O requests

## Slide 8: Internal Components of a Modern SSD
Back End: data storage
  Memory chips (e.g., NAND flash memory, PCM, MRAM, 3D XPoint)
Front End: management and control units
  Host–Interface Logic (HIL): protocol used to communicate with host
  Flash Translation Layer (FTL): manages resources, processes I/O requests
  Flash Channel Controllers (FCCs): sends commands to, transfers data with memory chips in back end

## Slide 9: Conventional Host–Interface Protocols for SSDs
SSDs initially adopted conventional host–interface protocols (e.g., SATA)
  Designed for magnetic hard disk drives
  Maximum of only thousands of IOPS per device
Process 1
Process 2
Process 3
OS Software Stack
SSD Device
Hardware dispatch queue
I/O Scheduler
In-DRAM
I/O Request
Queue

## Slide 10: Host–Interface Protocols in Modern SSDs
Modern SSDs use high-performance host–interface protocols (e.g., NVMe)
  Bypass OS intervention: SSD must perform scheduling
  Take advantage of SSD throughput: enables millions of IOPS per device
OS Software Stack
Hardware dispatch queue
Process 1
Process 2
Process 3
SSD Device
I/O Scheduler
In-DRAM
I/O Request
Queue
Fairness mechanisms in OS software stack are also eliminated
Do modern SSDs need to handle fairness control?

## Slide 11: Background: Modern SSD Design Unfairness Across Multiple Applications in Modern SSDs FLIN: Flash-Level INterference-aware SSD Scheduler Experimental Evaluation Conclusion
Outline

## Slide 12: Measuring Unfairness in Real, Modern SSDs
We measure fairness using four real state-of-the-art SSDs
  NVMe protocol
  Designed for datacenters
Flow: a series of I/O requests generated by an application
Slowdown = (lower is better)
Unfairness = (lower is better)
Fairness = (higher is better)
shared flow response time
alone flow response time
max slowdown
min slowdown
1
unfairness

## Slide 13: Representative Example: tpcc and tpce
average slowdown of tpce: 2x to 106x across our four real SSDs
tpce
tpcc
very low fairness
SSDs do not provide fairness among concurrently-running flows

## Slide 14: What Causes This Unfairness?
Interference among concurrently-running flows
We perform a detailed study of interference
  MQSim: detailed, open-source modern SSD simulator [FAST 2018] https://github.com/CMU-SAFARI/MQSim
  Run flows that are designed to demonstrate each source of interference
  Detailed experimental characterization results in the paper
We uncover four sources of interference among flows

## Slide 15: Source 1: Different I/O Intensities
The I/O intensity of a flow affects the average queue wait time of flash transactions
The queue wait time
highly increases with I/O intensity

## Slide 16: Source 1: Different I/O Intensities
An experiment to analyze the effect of concurrently executing two flows with different I/O intensities on fairness
  Base flow: low intensity (16 MB/s) and low average chip-level queue length
  Interfering flow: varying I/O intensities from low to very high
The average response time of a low-intensity flow substantially increases due to
interference from a high-intensity flow

## Slide 17: Source 2: Different Access Patterns
Some flows take advantage of chip-level parallelism in back end
Leads to a low queue wait time
Even distribution of transactions in chip-level queues

## Slide 18: Source 2: Different Request Access Patterns
Other flows have access patterns that do not exploit parallelism

## Slide 19: Source 2: Different Request Access Patterns
An experiment to analyze the interference between concurrent flows with different access patterns
  Base flow: streaming access pattern (parallelism friendly)
  Interfering flow: mixed streaming and random access pattern
Flows with parallelism-friendly access patterns are susceptible to interference from flows whose access patterns do not exploit parallelism

## Slide 20: Source 3: Different Read/Write Ratios
State-of-the-art SSD I/O schedulers prioritize reads over writes
When flows have different read/write ratios, existing schedulers do not effectively provide fairness

## Slide 21: Source 4: Different Garbage Collection Demands
NAND flash memory performs writes out of place
  Erases can only happen on an entire flash block (hundreds of flash pages)
  Pages marked invalid during write
Garbage collection (GC)
  Selects a block with mostly-invalid pages
  Moves any remaining valid pages
  Erases that block
High-GC flow: flows with a higher write intensity induce more garbage collection activities

## Slide 22: Source 4: Different Garbage Collection Demands
Garbage collection may block user I/O requests
  Primarily depends on the write intensity of the workload
An experiment with two 100%-write flows with different intensities
  Base flow: low intensity and moderate GC demand
  Interfering flow: different write intensities from low-GC to high-GC
Lower fairness
due to GC execution
Tries to
preempt GC
The GC activities of a high-GC flow can
unfairly block flash transactions of a low-GC flow

## Slide 23: Summary: Source of Unfairness in SSDs
Four major sources of unfairness in modern SSDs
  I/O intensity
  Request access patterns
  Read/write ratio
  Garbage collection demands
OUR GOAL
Design an I/O request scheduler for SSDs that (1) provides fairness among flows by mitigating all four sources of interference, and (2) maximizes performance and throughput
Notes: New goal, link to sources

## Slide 24: Background: Modern SSD Design Unfairness Across Multiple Applications in Modern SSDs FLIN: Flash-Level INterference-aware SSD Scheduler Experimental Evaluation Conclusion
Outline

## Slide 25: FLIN: Flash-Level INterference-aware Scheduler
FLIN is a three-stage I/O request scheduler
  Replaces existing transaction scheduling unit
  Takes in flash transactions, reorders them, sends them to flash channel
Identical throughput to state-of-the-art schedulers
Fully implemented in the SSD controller firmware
  No hardware modifications
  Requires < 0.06% of the DRAM available within the SSD
Notes: Fix animation

## Slide 26: Three Stages of FLIN
Stage 1: Fairness-aware Queue Insertion relieves I/O intensity and access pattern interference
9
8
7
6
5
4
3
2
1
0
From high-intensity flows
From low-intensity flows
Head
Tail

## Slide 27: Three Stages of FLIN
Stage 1: Fairness-aware Queue Insertion relieves I/O intensity and access pattern interference
Stage 2: Priority-aware Queue Arbitration enforces priority levels that are assigned to each flow by the host

## Slide 28: Three Stages of FLIN
Stage 1: Fairness-aware Queue Insertion relieves I/O intensity and access pattern interference
Stage 2: Priority-aware Queue Arbitration enforces priority levels that are assigned to each flow by the host
Stage 3: Wait-balancing Transaction Selection relieves read/write ratio and garbage collection demand interference

## Slide 29: Background: Modern SSD Design Unfairness Across Multiple Applications in Modern SSDs FLIN: Flash-Level INterference-aware SSD Scheduler Experimental Evaluation Conclusion
Outline

## Slide 30: Evaluation Methodology
MQSim: https://github.com/CMU-SAFARI/MQSim [FAST 2018]
  Protocol: NVMe 1.2 over PCIe
  User capacity: 480GB
  Organization: 8 channels, 2 planes per die, 4096 blocks per plane, 256 pages per block, 8kB page size
40 workloads containing four randomly-selected storage traces
  Each storage trace is collected from real enterprise/datacenter applications: UMass, Microsoft production/enterprise
  Each application classified as low-interference or high-interference

## Slide 31: Two Baseline Schedulers
Sprinkler [Jung+ HPCA 2014] a state-of-the-art device-level high-performance scheduler
Sprinkler+Fairness [Jung+ HPCA 2014, Jun+ NVMSA 2015] we add a state-of-the-art fairness mechanism to Sprinkler that was previously proposed for OS-level I/O scheduling
  Does not have direct information about the internal resources and mechanisms of the SSD
  Does not mitigate all four sources of interference

## Slide 32: FLIN Improves Fairness Over the Baselines
Chart: Fraction of High-Intensity Traces in Workload
| 0.25 | 0.5 | 0.75 | 1
Sprinkler | 0.495 | 0.31 | 0.095 | 0.01
Sprinkler+Fairness | 0.7 | 0.49 | 0.225 | 0.13
FLIN | 0.91 | 0.88 | 0.53 | 0.39
FLIN improves fairness by an average of 70%, by mitigating all four major sources of interference

## Slide 33: FLIN Improves Performance Over the Baselines
Chart: Fraction of High-Intensity Traces in Workload
| 0.25 | 0.5 | 0.75 | 1
Sprinkler | 2.5 | 1.495 | 0.75 | 0.5
Sprinkler+Fairness | 2.8 | 1.9 | 1.2 | 0.7
FLIN | 3.45 | 2.6 | 1.7 | 1.3
FLIN improves performance by an average of 47%, by making use of idle resources in the SSD and improving the performance of low-interference flows

## Slide 34: Other Results in the Paper
Fairness and weighted speedup for each workload
  FLIN improves fairness and performance for all workloads
Maximum slowdown
  Sprinkler/Sprinkler+Fairness: several applications with maximum slowdown over 500x
  FLIN: no flow with a maximum slowdown over 80x
Effect of each stage of FLIN on fairness and performance
Sensitivity study to FLIN and SSD parameters
Effect of write caching

## Slide 35: Background: Modern SSD Design Unfairness Across Multiple Applications in Modern SSDs FLIN: Flash-Level INterference-aware SSD Scheduler Experimental Evaluation Conclusion
Outline

## Slide 36: Conclusion
Modern solid-state drives (SSDs) use new storage protocols (e.g., NVMe) that eliminate the OS software stack
  Enables high throughput: millions of IOPS
  OS software stack elimination removes existing fairness mechanisms
  Highly unfair slowdowns on real state-of-the-art SSDs
FLIN: a new I/O request scheduler for modern SSDs designed to provide both fairness and high performance
  Mitigates all four sources of inter-application interference
    Different I/O intensities
    Different request access patterns
    Different read/write ratios
    Different garbage collection demands
  Implemented fully in the SSD controller firmware, uses < 0.06% of DRAM
  FLIN improves fairness by 70% and performance by 47% compared to a state-of-the-art I/O scheduler (Sprinkler+Fairness)

## Slide 37: P&S Modern SSDs FLIN: Enabling Fairness and Enhancing Performance in Modern NVMe Solid State Drives
Arash Tavakkol, Mohammad Sadrosadati, Saugata Ghose,
Jeremie S. Kim, Yixin Luo, Yaohua Wang, Nika Mansouri Ghiasi,
Lois Orosa, Juan Gómez-Luna, Onur Mutlu
ISCA 2018